Springboot3 course documentation

## Inversion of control (IoC)
The approach of outsourcing the construction and management of objects. It’a a design principle.
## Dependency injection (DI)
It’s a specific technique used to implement the IoC. The class does not create its dependencies, but rather receives them from an external source.

## Types of injection
Constructor injection: recommended. Use it for required dependencies. If there is only one constructor, the @autowired annotation it’s optional.
//Constructor Injection @Autowired public DemoController(Coach theCoach, Player thePlayer){ myCoach = theCoach; myPlayer = thePlayer; }

- Setter injection: Use it for optional dependencies. If the dependency is not provided, the app can provide default logic.

@Autowired public void setCoach(Coach theCoach){ myCoach = theCoach; } / // The setter can get any name / @Autowired public void initCoach(Coach theCoach){ myCoach = theCoach; } / @Autowired(required = false) public void setPlayer(Player thePlayer){ / // default logic if (thePlayer == null) { logger.error("thePlayer is null, initialization failed."); return; // No initialice myPlayer if thePlayer is null } myPlayer = thePlayer; }

Field injection: Not recommended by Spring Team.

## Spring Autowiring
Used for dependency injection. Spring will look for an annotated class that matches by type (class or interface and will inject it directly.
@Component annotation marks the class as an Spring Bean, that’s it a class that can be managed by Spring. Makes the class available for dependency injection.

## Spring Scan
Spring will scan all the classes in all the @SpringbootApplication annoted class packege and sub-packages.
How scan packages outside the @SpringbootApplication scope:
@SpringBootApplication(scanBasePackages = {"com.example.demo","com.example.demo2"})
## @SpringBootApplication
It’s composed by other annotations:
- @EnableAutoConfiguration: enable Spring boot’s autoconfiguration support.
- @ComponentScan: enable component scanning for the current package and sub-packages.
- @Configuration: able to register extra beans with the @Bean annotation and other configuration classes.